## Slide 1
मध्यपश्चिम विश्वविद्यालय
MID-WESt UNIVERSITY
Presentation .
Name=Kamal Bdr Rawal

## Slide 2: Canonical forms

## Slide 3
Definition: Any Boolean function that is expressed as a sum of minterms or as a product of maxterms is said to be in its canonical form. To convert from one canonical form to another, interchange the symbols Σ and Π, and list the index numbers that were excluded from the original form.

## Slide 4: Canonical SoP and PoS forms
A truth table consists of a set of inputs and outputs𝑠. If there are ‘n’ input variables, then there will be 2n possible combinations with zeros and ones. So the value of each output variable depends on the combination of input variables. So, each output variable will have ‘1’ for some combination of input variables and ‘0’ for some other combination of input variables. Therefore, we can express each output variable in following two ways.
Canonical SoP form
Canonical PoS form

## Slide 5
Sum of Minterms (Sum of Products or SOP)
We have seen, one can obtain 2" distinct minterms form n binary input variables and that any Boolean function can be expressed as a sum of minterms. The minterms whose sum defines the Boolean function are those that give the 1's of the function in a truth table. It is sometimes convenient to express the Boolean function in its sum of minterms form. If not in this form, it can be made so by first expanding the expression into a sum of AND terms. Each term is then inspected to see if it contains all the variables. If it misses one or more variables, it is ANDed with an expression such as x + x, where x is one of the missing variables.

## Slide 6
Question: Express the Boolean function in a sum of minterms.
Solution: The function has three variables A, B, and C.
The first term A is missing two variables; therefore:
A=A (B+B') = AB + AB‘ [B is missing variable]
This is still missing one variable C, so A = AB(C+C') + AB'(C+C') = ABC+ABC' +
AB'C + AB'C'
The second term B'C is missing one variable: B'C=B'C(A + A') = AB'C + A'B'C
Combing all terms, we have F =A+B'C ABC+ABC+AB'C+AB'C' + AB'C+A'B'C
But AB'C appears twice, and according to THEOREM 1 of Boolean algebra
x + x = x, it is possible to remove one of them. Rearranging the minterms in
ascending order, we finally obtain:
F=A'B'C+AB'C' AB'C+ABC+ ABC
= m1+m4+m5+m6+m7,
Shorthand notation,
F(A, B, C) = (1, 4, 5, 6, 7)
The summation symbol ∑ stands for the ORing of terms: the numbers following
it are the minterms of the function.

## Slide 7
An alternate procedure for deriving the minterms of a Boolean function is to obtain the truth table of the function directly from the algebraic expression and then read the minterms from the truth table.
Truth table for f=A+B’C
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Truth table for F=A+B'C, from the truth table, we can then read the five minterms of the function to be 1, 4, 5, 6, and 7.

## Slide 8
Product of Maxterms (Product of Sums or POS)
Each of the 22" functions of n binary variables can be also expressed as a product of maxterms. To express the Boolean function as a product of maxterms, it must first be brought into a form of OR terms. This may be done by using the distributive law, xyz = (x+y)(x+z). Then any missing variable x in each
OR term is ORed with xx'. This procedure is clarified by the following example:

## Slide 9
Question: Express the Boolean function F = xy + x'z in a product of maxterm form.
Solution:
First, convert the function into OR terms using the distributive law: F=xy+x’z = (xy+x') (xy+z)
= (x + x')(y+x') (x+z)(y+z)
= (x’+y)(x+z)(y+z)
The function has three variables: x, y, and z. Each OR term is missing one variable; therefore:
x' + y = x' + y + ZZ‘ = (x' + y + Z)(x' + y + z')
x+z=x +z +yy’ = (x+y+z)(x+y’+z)
y+z =y+z+xx' = (x+y+z) (x’ + y + z)
Combing all maxterms and removing repeated terms: F=(x+y+z)(x+y’+z)(x’+y+z)(x’+y+z’)
=M0M2M4M5
Shorthand notation:
F(x, y, z) = Pi(0, 2, 4, 5)
The product symbol I denotes the ANDing of maxterms; the numbers are the maxterms of the function.

## Slide 10
Conversion between canonical forms
The complement of a function expressed as the sum of minterms equals the sum of minterms missing from the original function.
For example: Consider the function, F(A, B, C) = Sigma(1, 4, 5, 6, 7)
Its complement can be expressed as:
F'(A, B, C) = ∑(0,2,3) = mo + m₂ + m3
Now, if we take the complement of F' by DeMorgan's theorem, we obtain Fin a different form:
F(A,B,C) = (m0 + m₂ + m3) = m0.m2.m3= M0. Μ2. Μ3 = (0,2,3)
The last conversion follows from the definition of min terms and maxterms that m' = M
General Procedure: To convert from one canonical form to another, interchange the symbols and Π and list those numbers missing from the original form. In order to find the missing terms, one must realize that the total number of minterms or maxterms is 2" (numbered as 0 to 2"), where n is the number of binary variables in the function.

## Slide 11
Consider a function, F = xy + X’Z First, we derive the truth table of the function
x | y | z | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
The minterms of the function are read from the truth table to be 1, 3, 6, and 7. The function expressed in sum of minterms is
F(x, y, z) = Sigma(1, 3, 6, 7)
Since there are a total of eight minterms or maxterms in a function of three variables, we determine the missing terms to be 0, 2, 4, and S. The function expressed in product of maxterm is
F(x, y, z) = prod (0, 2, 4, 5)

## Slide 12
Thank you..